Nimrod System

Documentation Paper No.2

Nimrod format for image

and model field files

# Author: David Stone/Dawn Harrison/R.Standing

Version:2.6 edited by Andrew C Bennett

### Date: last updated 21 May 2013

Nimrod File Format

With the exception of raw observations and some constants, most files on the Nimrod system will be held in a standard format developed from the NDG format.

Each file consists of one or more records held in sequential format. Each record consists of a 512 byte header followed by a data array. The data array may be in integer format with 1,2 or 4 bytes per item or in real format with 4 bytes per item.

Each header and data block are bounded by Fortran housekeeping bytes consisting of a 4-byte integer describing the length of the block. For the header, this integer is always 512. For the data, this will be {number of columns} x {number of rows} x {Number of bytes for each data element}. The file therefore looks like this:

<Header block length><Header block><Header block length><Data block length><Data block><Data block length><EOF>

All Nimrod format files contain big-endian data.

The default values for each element of the header will be; -32767 for integer elements, -32767.0 for real elements, and a 'null' string for character elements. It is recommended that all input data files have their data origin at the top left hand corner whenever possible. However, routines for reading the contents of Nimrod files will contain the option to return a data array with the first element being either the top left or bottom left point of the image/field. The header is constructed as follows.

| Data Type | Element number | Description of header element |
| --- | --- | --- |

| Integer*2 | 1-31 | General header entries (Bytes 1-62) |
| --- | --- | --- |
| I*2 | 1. | VT year. VT is the Validity Time of the data. For data with a time-period of validity (e.g. precip accumulation over one hour), this is the end of the time-period. |
| I*2 | 2. | VT month. |
| I*2 | 3. | VT day. |
| I*2 | 4. | VT hour. |
| I*2 | 5. | VT minute. |
| I*2 | 6. | VT second. |
| I*2 | 7. | DT year. DT is the Data Time. It can be used for models, forecast images, or forecast data. |
| I*2 | 8. | DT month. |
| I*2 | 9. | DT day. |
| I*2 | 10. | DT hour. |
| I*2 | 11. | DT minute. |
| I*2 | 12. | =0 if data is of type real, =1 if data is of type integer, =2 if data is of type byte. |
| I*2 | 13. | Number of bytes for each data element (1, 2, or 4). |
| I*2 | 14. | Experiment number (user supplied) – must be a multiple of four. 0 for operational output. Number +1 for QV-nowcast and Number+2 for CDP outputs |
| I*2 | 15. | Horizontal grid type (0=NG, 1=lat/lon, 2=space view, 3=polar stereographic, 4=UTM32 (EuroPP), 5=Rotated Lat Lon, 6=other). |
| I*2 | 16. | Number of rows in field. |
| I*2 | 17. | Number of columns in field. |
| I*2 | 18. | Header file release number (2 for the first release of the Nimrod header). |
| I*2 | 19. | Field code number (includes data type). |
| I*2 | 20. | Vertical co-ordinate type (0=height above orography, 1=height above sea-level, 2=pressure, 3=sigma, 4=eta, 5=radar beam number, 6=temperature, 7=potential temperature, 8=equivalent potential temperature, 9=wet bulb potential temperature, 10=potential vorticity, 11=cloud boundary, 12=levels below ground). |
| I*2 | 21. | Vertical co-ordinate of reference level eg. for thickness fields (values as for element 20). |
| I*2 | 22. | Number of elements, starting at element 60, which are used for data-specific information eg. calibration information only appropriate to a radar image. (this element previously indicated whether or not a supplied colour table is used). |
| I*2 | 23. | Number of elements, starting at element 109, which are used for data-specific information (previously this was the number of categories in colour table). |
| I*2 | 24. | Location of origin of data (0=top LH corner, 1=bottom LH corner, 2=top RH corner, 3=bottom RH corner). |
| I*2 | 25. | Integer missing data value. |
| I*2 | 26. | Period of interest for accumulation, average or probability (minutes) A value of +32767 indicates that element 159 holds this value in seconds rather than minutes. |
| I*2 | 27. | Number of Model Levels available for this parameter |
| I*2 | 28. | Projection biaxial ellipsoid [ 0 = Airy 1830 (NG), 1 = International 1924 (modified UTM-32), 2 = GRS80 (GUGiK 1992/19) ]. |
| I*2 | 29. | Ensemble member ID |
| I*2 | 30. | Origin model ID (1: nowcast, 2: radar, 11:UKV, 12:UK4, 13:NAE, 14:Global, 15:MOGREPS-EU, 16:MOGREPS-UK, 17:UK4-extended, 18:4km Italy UM |
| I*2 | 31. | Time averaging (LBPROC) Combinations of: 1: warm bias applied 2: cold bias applied 4: smoothed 8: only observations used 16: averaged over multiple surface types 32: scaled to UM resolution (e.g. winds) 128: accumulation or average 256: extrapolation 512: time-lagged 4096: minimum in period 8192: maximum in period |
| Real*4 | 32-59 | General header entries (Bytes 63-174) |
| R*4 | 32. | Value of vertical co-ordinate (eg. 500.0 for a 500hPa height field), or radar beam number (8888.0=sea-level, 9999.0=ground level or undefined). If the vertical co-ordinate type (element 20) is set to 3 or 4 then the value is set to model level number. For example, 3.0 for model level three or 2.5 for model level two and a half. |
| R*4 | 33. | Value of reference vertical co-ordinate (eg. 1000.0 for a 500 - 1000hPa thickness field) |
| R*4 | 34. | Northing or latitude or start line of first row of data (metres for NG, degrees for PS grids). |
| R*4 | 35. | Interval between rows ie. pixel size. For PS images this will be the resolution in the y-direction at the standard latitude of 60 degrees North (metres or degrees). |
| R*4 | 36. | Easting or longitude or start pixel of first point of first row of data (metres or degrees). |
| R*4 | 37. | Interval between columns ie. pixel size. For polar stereographic images this will be the resolution in the x-direction at the standard latitude of 60 degrees North (metres or degrees). |
| R*4 | 38. | Real missing data value. |
| R*4 | 39. | MKS scaling factor for data (=100.0 for pressure in millibars). |
| R*4 | 40. | Data offset value. |
| R*4 | 41. | X-offset of model data from gridpoints (positive = to East, negative = to West). |
| R*4 | 42. | Y-offset of model data from gridpoints (positive = to North, negative = to South) |
| R*4 | 43. | Standard latitude or latitude of true origin(TM or PS projection) in degrees |
| R*4 | 44. | Standard longitude or longitude of true origin(TM or PS projections) in degrees |
| R*4 | 45. | Easting of true origin (TM Projection) in metres |
| R*4 | 46. | Northing of true origin (TM Projection) in metres |
| R*4 | 47 | Scale factor on central meridian for TM Projections [ NG = 0.9996012717, modified UTM-32 = 0.9996, GUGiK 1992/19 = 0.9993 ]. |
| R*4 | 48 | Threshold value (e.g. for probabilities and percentiles). |
| R*4 | 49 - 59. | To be used for general header entries. |
| Real*4 | 60-104 | Data specific header entries (Bytes 175-354) These elements were previously used for a colour table. |
| R*4 | 60 | Northing or latitude of top left corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 61 | Easting or longitude of top left corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 62 | Northing or latitude of top right corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 63 | Easting or longitude of top right corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 64 | Northing or latitude of bottom right corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 65 | Easting or longitude of bottom right corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 66 | Northing or latitude of bottom left corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 67 | Easting or longitude of bottom left corner of the image (metres for NG, degrees for PS grids) |
| R*4 | 68 | Satellite calibration co-efficient |
| R*4 | 69 | Space count (satellite data) |
| R*4 | 70 | Ducting Index |
| R*4 | 71 | Elevation Angle |
| R*4 | 72 | Neighbourhood size (km) for probabilities |
| R*4 | 73 | Radius of interest (km) for probabilities |
| R*4 | 74 | Recursive filter strength  (for probabilities) |
| R*4 | 75 | Fuzzy threshold parameter |
| R*4 | 76 | Fuzzy duration of occurrence |
| R*4 | 77-104 | Spare |
| Character | 105-107 | Character header entries (Bytes 355-410) |
| C*8 | 105. | Character string denoting the units of the field. |
| C*24 | 106. | Character string to describe the source of the data. |
| C*24 | 107. | Title of field. |
| Integer*2 | 108-159 | Data specific header entries (Bytes 411-512) Table 1: Radar-specific entries |
| I*2 | 108. | The radar number for a single site image (set to zero for a radar composite). |
| I*2 | 109. | The radar sites which have gone into forming a composite image. Each site is represented by a particular bit which is set to 1 if the site was available, and 0 if it was not. Radar site 1 will be represented by the least significant bit of element 109. |
| I*2 | 110. | As element 110 for additional radar sites. This will only be required if the number of operational sites exceeds 16. |
| I*2 | 111. | Clutter map number. |
| I*2 | 112. | Calibration Type (0=uncalibrated, 1=frontal, 2=showers, 3=rain shadow, 4=bright band ; the negatives of these values can be used to indicate a calibration which has subsequently been removed. |
| I*2 | 113. | Bright band height (units of 10m). |
| I*2 | 114. | Bright band intensity. This is defined as the enhancement of the rainfall in the bright band relative to the rain beneath it. |
| I*2 | 115. | Bright band test parameter 1. This is the percentage of sectors (24 in all) which have detected a possible bright band. |
| I*2 | 116. | Bright band test parameter 2. This is the percentage of the sectors in entry 30 which agree with the bright band height of 28. |
| I*2 | 117. | Infill Flag (for level 4.1) |
| I*2 | 118. | Stop Elevation (for level 4.1) |
| I*2 | 119-131 | Used to duplicate real*4 general header entries 32-44 for data transfers to COSMOS (Note: All entries are ×10-3). |
| I*2 | 132-139 | Used to duplicate real*4 specific header entries 60-67 for data transfers to COSMOS (Note: All entries are ×10-3). |
| I*2 | 140 | Sensor identifier (Satellite data) |
| I*2 | 141 | Meteosat identifier (currently 5 or 6) |
| I*2 | 143 | Availability of synop meteosat and forecast alphas in combined alphas field (e.g 111 all available, 100, only synop) |
| etc. |  | The remaining space may be used for further data/application-specific entries. |
| I*2 | 159 | Period of interest for accumulation, average or probability (seconds) Only used when element 26 is set to +32767 |
| Integer*2 | 108-159 | Data specific header entries (Bytes 411-512) Table 2: Probability-specific entries (when element 48 is set) |
| I*2 | 108. | Indicator of threshold type specified in element 48 1: probability of event greater than threshold 2: probability of event less than threshold 3: distribution percentile threshold |
| I*2 | 109. | Probability method. Combinations of: 1: AOT (At any one time) over a time window of interest (this is the average probability over the time window) 2: ST (SomeTime) over the time window of interest (this is the maximum probability over the time window) 4: AT (All Time) over a time window of interest (this the probability that the threshold will (not) be exceeded for a certain total duration over the time window). 8: AOL (Any One Location over the region of interest (this is the average probability over the region) 16: SW (SomeWhere) over the region of interest (this is the maximum probability over the region) |
| I*2 | 110. | Number of iterations of the recursive filter |
| I*2 | 111. | Number of ensemble members this field represents |
| I*2 | 112. | Duration of occurrence in window of interest (window of interest is element 26) |
| etc. |  | The remaining space may be used for further data/application-specific entries. |
| I*2 | 159 | Period of interest for accumulation, average or probability (seconds) Only used when element 26 is set to +32767 |
| Integer*2 | 108-159 | Data specific header entries (Bytes 411-512) Table 3: Tile surface specifications |
| I*2 | 114. | Indicator of surface tile type 1 Broadleaf Tree 2 Needleleaf Tree 3 C3 Grass 4 C4 Grass 5 Crop (Not available from UM – MOSES only) 6 Shrub 7 Urban 8 Water 9 Soil 10 Ice |
| Integer*2 | 108-159 | Data specific header entries (Bytes 411-512) Table 4: Radiation type specifications |
| I*2 | 115. | Indicator of radiation type. Combinations of: 2 clear-sky radiation 4 direct radiation 8 diffuse radiation 16 downward radiation 32 upward radiation 64 instantaneous ("corrected") |

Notes :

1.	The field code number (19) will identify the type of data. For example, Meteosat IR readings or weather radar returns. Numbers 1-400 are reserved for unified model field codes as used in (CF) FieldsFiles. A list of field type codes is as appendix A.

2.	The grid descriptor elements in the header (elements 34 & 36) will refer to the location of the centre of the pixel for image data, and to the gridpoint position for model data. Wind components u & v are often 'staggered' in model grids, the appropriate X and Y offsets must be specified in elements 41 and 42 of the header.

The DT (Data Time) specified in elements 7 to 11 should be set to -32767 for basic images. For forecast images, DT will refer to the time of the base image from which forecasts are done. For model files, T+0 initial fields should have DT equal to VT, in forecast fields DT will refer to the T+0 initial field from which forecasts are made.

3.	In handling polar stereographic images, it is assumed that the South Pole is the reference pole, the standard latitude is given in entry 43, and the downward longitude in entry 40. The origin of the image is specified by latitude and longitude in entries 34 & 36. These values, together with the resolution at standard latitude (entries 35 & 37), and the number of rows and columns in the field (entries 16 & 17), are enough to completely define a PS image.

4.	The above scheme preserves the generality of the first section of the header. Elements 1 to 31 are I*2 entries which are not data or application-specific. It is proposed that elements 32 to 59 inclusive should be similarly reserved R*4 entries. The data-specific elements should thus be placed in elements 60-104 if they are Real, and beginning at element 108 if they are integer.

Appendix A

Field code numbers

Red entries indicate changes to a field code at versions 2.4 and 2.5 of this document

Blue entries indicate field codes not in use as of version 2.4 of this document

The Filename tag column indicates the Met Office file each field is stored in

| Field code | Description | Filename tag |
| --- | --- | --- |
| 2 | 3D Height | height |
| 3 | 3D Temperature | temperature |
| 4 | 850hPa w-bulb pot temp | temperature |
| 5 | Wind U | winduv |
| 5 | Wind U smoothed |  |
| 6 | Wind V | winduv |
| 6 | Wind V smoothed |  |
| 8 | RH | relhumidity |
| 12 | MSLP | pressure |
| 13 | Pressure anomaly | pressure |
| 18 | Surface temperature | soil |
| 24 | Sea surface temperature | sst |
| 27 | Snow fraction | preciptype |
| 28 | Snow probability | preciptype |
| 29 | Fog probability | fog |
| 50 | Freezing level | height |
| 58 | Screen temperature | temperature |
| 61 | Precip accumulation | precipaccum |
| 63 | Precip rate | precip |
| 64 | Dynamic rain rate | precip |
| 65 | Dynamic snow rate | precip |
| 66 | Convective rain rate | precip |
| 67 | Convective snow rate | precip |
| 73 | Orography | height |
| 74 | Coastline (land-sea mask) |
| 79 | 3D Cloud | cloud |
| 80 | Cloud top brightness temperature |
| 86 | Convective cloud cover | cloud |
| 87 | Convective cloud base | cloud |
| 88 | Convective cloud top | cloud |
| 89 | Cloud top temperature | cloud |
| 90 | Total sunshine | radiation |
| 91 | Radiation (SW) | radiation |
| 92 | Radiation (LW) | radiation |
| 93 | Radiation (total) | radiation |
| 94 | Unused |  |
| 95 | Unused |  |
| 96 | Radiation (UV) | radiationuv |
| 100 | Critical precip rate | snow |
| 101 | Snow melting level (ASL) | frzlev |
| 102 | Rain level (ASL) | frzlev |
| 121 | Snow depth | snow |
| 122 | Screen water temperature | visibility |
| 133 | Screen total water content | visibility |
| 144 | Screen vapour pressure | soil |
| 154 | Screen dew point temperature | temperature |
| 155 | Obs vis screen | visibility |
| 155 | Visibility | visibility |
| 156 | Worst visibility | visibility |
| 157 | Obs fog mask | visibility |
| 161 | Cloud base height | cloud |
| 172 | Cloud cover | cloud |
| 173 | Low/Med/High Cloud cover | cloudcomp |
| 174 | Low/Med/High Cloud cover for VW | cloudcomp |
| 185 | Snow melt | snow |
| 190 | Soil temperature | soil |
| 191 | Soil moisture | soil |
| 192 | Unfrozen soil water | soil |
| 193 | Frozen soil water | soil |
| 194 | Soil moisture deficit | soil |
| 195 | Surface run-off | surfroff |
| 196 | Total run-off | soil |
| 197 | Potential evaporation | soil |
| 198 | Evaporation | soil |
| 199 | Excess precipitation | soil |
| 200 | Subsurface run-off | subsroff |
| 201 | Soil moisture availability | soil |
| 202 | Surface conductance | soil |
| 203 | Surface/canopy water | soil |
| 204 | Evapotranspiration from soil | soil |
| 205 | Pressure | pressure |
| 206 | Wet bulb freezing level | frzlev |
| 207 | Cloud top height | cloud |
| 208 | CAPE | cape |
| 209 | Orographic roughness | ancil |
| 210 | Nominal half-peak-to-trough | ancil |
| 213 | Precipitation rate | precip |
| 214 | Precipitation accumulation | precip |
| 215 | HRA catchment maps | ancil |
| 216 | Accumulation warnings |  |
| 217 | Radar data in dbZ |  |
| 218 | Snowfall accumulation | soil |
| 219 | Rainfall accumulation | soil |
| 221 | Aerosol | visibility |
| 222 | Downwind sectors |  |
| 230 | MODIS |  |
| 231 | MODIS |  |
| 232 | MODIS |  |
| 233 | MODIS |  |
| 234 | MODIS |  |
| 235 | MODIS |  |
| 236 | MODIS |  |
| 261 | FSI |  |
| 262 | FSI |  |
| 263 | FSI |  |
| 264 | FSI |  |
| 265 | FSI |  |
| 266 | FSI |  |
| 300 | Boundary layer height | height |
| 301 | Tile surface temperature | soil |
| 302 | Tile screen temperature | soil |
| 303 | Sensible surface heat flux | radiation |
| 310 | River flow | rivers |
| 311 | River flood indicator | rivers |
| 312 | River depth | rivers |
| 313 | River width | rivers |
| 314 | River flow in | rivers |
| 315 | River base flow in | rivers |
| 316 | Surface store | rivers |
| 317 | Subsurface store | rivers |
| 401 | Satellite |  |
| 402 | Satellite |  |
| 403 | Satellite |  |
| 404 | IR cloud top temperature |  |
| 405 | Satellite rain rate |  |
| 406 | Satellite |  |
| 407 | Satellite snow cover |  |
| 410 | Rain forecast area map |  |
| 420 | Rain fraction |  |
| 421 | Precipitation type | preciptype |
| 422 | Lightning rate | convection |
| 423 | Snow probability | snow |
| 424 | Riming rate | snow |
| 425 | Prob of rain | probofrain |
| 426 | Prob of rain > 0.5mm/hr |  |
| 427 | Prob of rain > 4.0mm/hr |  |
| 428 | Prob of large hail |  |
| 429 | Prob of tornado |  |
| 430 | Prob of severe thunderstorm |
| 431 | Hail size |  |
| 450 | Area of raar coverage |  |
| 451 | Prob of no rain |  |
| 452 | Prob of anaprop |  |
| 453 | Orographic enhancement | precip |
| 454 | Radar beam infilling map |  |
| 455 | Radar anaprop climatology |
| 456 | Radar heirarchy map |  |
| 457 | Radar domain map |  |
| 458 | Radar weights field |  |
| 459 | Radar overlap maps |  |
| 501 | Wind speed shear | convwind |
| 502 | Absolute helicity | convection |
| 503 | Tornado index | convection |
| 504 | Directional wind shear | convwind |
| 505 | CAPE | cape |
| 506 | Precipitable water | convection |
| 507 | Lifted index | convection |
| 508 | Low level jet U&V | convwind |
| 514 | Low level jet V component | convwind |
| 509 | Low level jet curvature | convwind |
| 510 | Lightning index | convection |
| 511 | Davies parameter | convection |
| 512 | Hail size | convection |
| 513 | Convective inhibition | cape |
| 599 | Triggered lightning | convection |
| 701 | Ozone | airquality |
| 702 | Nitric Oxide | airquality |
| 704 | Nitrogen Dioxide | airquality |
| 710 | Carbon Monoxide | airquality |
| 771 | Sulphur Dioxide | airquality |
| 772 | PM10 (large particles) | airquality |
| 773 | PM2.5 (small particles) | airquality |
| 774 | Air quality index | airquality |
| 800 | Peak convective gust | convwind |
| 801 | Wind gust (knots) | wind |
| 802 | Wind gust (beaufort) | wind |
| 803 | Wind U&V | wind |
| 804 | Wind speed (knots) | wind |
| 805 | Wind speed (beaufort) | wind |
| 806 | Wind direction | wind |
| 807 | Pressure anomaly | pressure |
| 808 | Pressure gradient anom for U wind | pwindproc |
| 809 | Pressure gradient anom for V wind | pwindproc |
| 810 | Vegetative roughness | pwindproc |
| 811 | Frictional velocity | pwindproc |
| 812 | Outer layer wind speed | pwindproc |
| 813 | Inner layer wind speed | pwindproc |
| 814 | Reference wind speed | pwindproc |
| 815 | Reference height | pwindproc |
| 816 | Wave number | pwindproc |
| 817 | Wind gust | wind |
| 818 | Geostrophic pressure gradient ratio |
| 819 | Geostrophic pressure gradient dir diff |
| 824 | Wind gust (shear) | wind |
| 820 | Wind hc | wind |
| 821 | Wind gust risk | wind |
| 822 | Wind speed | wind |
| 823 | Roughness adjustment mask | wind |
| 900 | Boundary layer height | height |
| 901 | Tile surface temperature | soil |
| 910 | Theta level 1 |  |
| 8229 | Unfrozen soil water | soil |
| 8230 | Frozen soil water | soil |

# Footnotes

`	This element was originally 2 real*4 elements in the NDG header. The numbering of subsequent elements has therefore changed.